## Slide 1: FAST and IMAGE Coincident Viewing
11/17/16 Tagup

## Slide 2: Ephem Status
FAST definitive Ephem provided by R. Strangeway
  Time span: 1996 234 10:30:00.000 to 2009 121 02:26:49.990
  SMA = 8300, ECC = 0.1898; INC = 82.97 (all the rest variable)
  Inertial nodal regression rate = -0.5 deg/day; solar apparent motion 0.986 deg/day; movement in SM Local Time ~1.5 deg/day
IMAGE definitive Ephem constructed piece-wise from data obtained from CDAWeb (http://cdaweb.sci.gsfc.nasa.gov/cgi-bin/eval2.cgi)
  Time span: 3/27/2000 00:00:55.000 to 12/19/2005 23:58:00.000
  SMA = 29,815.4; ECC = 0.7531; INC = 90.010 (all the rest variable)

## Slide 3: IMAGE Epoch Filtering Strategy
Want time spans when IMAGE is within 30 degrees of apogee
Define ‘apogee’ vector
Calculate and filter
IMAGE Orbit
– angle between and

## Slide 4: FAST Epoch Filtering Strategy
Want FAST’s orbital plane (ascending and descending node) within 20:00 and 02:00 local time in SM coordinates (SMLT)
Calculate FAST’s angular momentum
Convert ECI components to SM and calculate corresponding SMLT
Filter on those times where SMLT() lies either in
  02:00-08:00
  14:00-20:00
Sun
FAST Orbit
(sunward)
12:00
02:00
20:00
08:00
14:00